## Slide 1: Segmentation of CT Lung Scans Using Image Processing Techniques
Terry Griffin
COMP.5230 Computer Vision I
Spring 2018

## Slide 2: The Problem
Lung cancer remains one of the leading causes of death
Computed tomography (CT) scans are very useful for lung cancer detection
Manually analyzing these scans is difficult
Computer-aided diagnosis systems can help in efficient early detection

## Slide 3: The Goal
From a CT chest scan:
1. Identify the two lungs
2. Separate the lungs into the five lobes

## Slide 4: CT Scan (the Input Data)
3 Dimensional image in MetaImage format
Signed 16-bit gray scale in Hounsfield units
Three datasets
  LOLA11 (55 scans)
  LUNA16 (100 scans)
  Tianchi (40 scans)
512x512 slices, usually 200-700 slices
Anisotropic

## Slide 5: Toolkit
C++
Insight Toolkit (ITK)
  Support for MetaImage format
  Full support for 3D image data
  Designed for working with medical images
Python for rapid prototyping and testing

## Slide 6: Lung Segmentation Approach
Thresholding to remove background and separate lungs from surrounding body mass
Separate the two lung volumes
Filtering to smooth the lung boundary and fill small internal holes

## Slide 7: Thresholding Step
Threshold out background at -3024
Find adaptive threshold to identify lungs and body mass
Use connected component analysis to identify lungs

## Slide 8: Separating the Left and Right Lung
Lungs are often very close together at a few places
Use dynamic programming to find a max cost path from bottom to top of each axial slice
If lungs are still connected in 3D, use erosion to remove connecting tissue

## Slide 9: Final Smoothing Step
Use dilation and erosion to smooth boundary and fill holes

## Slide 10: Evaluation
Manual checking of axial and coronal middle slices for LOLA11 and Tianchi scans
  All scans were segmented correctly
Quantiative comparison with reference segmentation for LUNA16 scans

## Slide 11: LUNA16 Scan Results
 | Overlap | Sensitivity | Specificity
Mean | 0.95 | 0.99 | 0.96
Min | 0.67 | 0.91 | 0.80
Max | 0.98 | 1.00 | 0.98
Std Dev | 0.04 | 0.01 | 0.02
Good overall performance
Preference for false positives over false negatives
A few lung masks had significant internal holes
False positive voxels form small ring around reference boundary

## Slide 12: Attempted Lobe Segmentation Method
Identify sheet-like fissures using Eigen values of Hessian matrix
Segment blood vessels and airways and construct distance maps
Combine image data, fissure measure, and distance maps into a cost image
Use a watershed algorithm to segment a lung into the lobes
Problem:
Could not get watershed algorithm to successfully segment lobes

## Slide 13: Conclusions
Lung segmentation using image processing techniques can be successful
Determining the correct set of processes and parameters is non-trivial
The parameters may depend on a particular dataset
Lobe segmentation is significantly more difficult than lung segmentation
Supposition: Deep learning may be a better approach

## Slide 14: Questions